Acid-Base Titration with Go Wireless pH and LabQuest 2

A titration is a process used to determine the volume of a solution needed to react with a given amount of another substance. In this experiment, you will titrate hydrochloric acid solution, HCl, with a basic sodium hydroxide solution, NaOH. The concentration of the NaOH solution is given and you will determine the unknown concentration of the HCl. Hydrogen ions from the HCl react with hydroxide ions from the NaOH in a one-to-one ratio to produce water in the overall reaction:

H+(aq) + Cl–(aq) + Na+(aq) +OH–(aq)  H2O(l) + Na+(aq) + Cl–(aq)

When an HCl solution is titrated with an NaOH solution, the pH of the acidic solution is initially low. As base is added, the change in pH is quite gradual until close to the equivalence point, when equimolar amounts of acid and base have been mixed. Near the equivalence point, the pH increases very rapidly, as shown in Figure 1. The change in pH then becomes more gradual again, before leveling off with the addition of excess base.

In this experiment, you will use a pH Sensor to monitor pH as you titrate. The region of most rapid pH change will then be used to determine the equivalence point. The volume of NaOH titrant used at the equivalence point will be used to determine the molarity of the HCl.

Figure 1

OBJECTIVES

In this experiment, you will

- Use a pH Sensor to monitor changes in pH as sodium hydroxide solution is added to a hydrochloric acid solution.

- Plot a graph of pH vs. volume of sodium hydroxide solution added.

- Use the graph to determine the equivalence point of the titration.

- Use the results to calculate the concentration of the hydrochloric acid solution.

MATERIALS

| Materials for both Method 1 (buret) and Method 2 (Drop Counter) |
| --- |
| LabQuest 2 with Bluetooth® Smart | magnetic stirrer or ring stand |
| LabQuest App (version 3.4 or newer) | stirring bar or Microstirrer |
| Go Wireless pH | wash bottle |
| HCl solution, unknown concentration | distilled water |
| ~0.1 M NaOH solution | 1 utility clamp or electrode support |
| pipet bulb or pump |  |
| 250 mL beaker |  |
| Materials required only for Method 1 (buret) |
| 50 mL buret | 2nd utility clamp |
| 10 mL pipet | 2nd 250 mL beaker |
| Materials required only for Method 2 (Drop Counter) |
| Vernier Drop Counter | 100 mL beaker |
| 60 mL reagent reservoir | 10 mL graduated cylinder |
| 5 mL pipet or graduated 10 mL pipet |  |

CHOOSING A METHOD

Method 1 has the student deliver volumes of NaOH titrant from a buret. After titrant is added, and pH values have stabilized, the student is prompted to enter the buret reading manually and a pH-volume data pair is stored.

Method 2 uses a Vernier Drop Counter to take volume readings. NaOH titrant is delivered drop by drop from the reagent reservoir through the Drop Counter slot. After the drop reacts with the reagent in the beaker, the volume of the drop is calculated, and a pH-volume data pair is stored.

METHOD 1: Measuring Volume Using a Buret

1.	Obtain and wear goggles.

2.	Use a pipet bulb (or pipet pump) to pipet 10 mL of the HCl solution into a 250 mL beaker. Add 50 mL of distilled water. DANGER: Handle the hydrochloric acid with care. It can cause painful burns if it comes in contact with the skin.

3.	Place the beaker on a magnetic stirrer and add a stirring bar. If no magnetic stirrer is available, you need to stir with a stirring rod during the titration.

4.	Set up Go Wireless pH.

- Ensure that the BNC connection between the Go Wireless Electrode Amplifier and the pH Electrode is secure.

- Press the power button on the Go Wireless Electrode Amplifier to turn it on. The LED on the sensor will flash red.

- Choose New from the File menu. On the Meter screen, choose Wireless Device Setup > Go Wireless… from the Sensors menu. Select your Go Wireless pH from the list of available sensors. When the sensor is paired with the software, the sensor LED will flash green.

5.	Set up the data-collection mode.

- On the Meter screen, tap Mode. Change the data-collection mode to Events with Entry.

- Enter the Name (Volume) and Units (mL). Select OK.

Figure 2

6.	Use an Electrode Support or a utility clamp to suspend the Go Wireless pH on a ring stand as shown in Figure 2. Position the tip of the electrode in the HCl solution and adjust its position so that it is not struck by the stirring bar.

7.	Obtain a 50 mL buret and rinse the buret with a few mL of the ~0.1 M NaOH solution. Record the precise concentration of the NaOH solution. Dispose of the rinse solution as directed by your teacher. Use a utility clamp to attach the buret to the ring stand as shown in Figure 2. Fill the buret a little above the 0.00 mL level of the buret with ~0.1 M NaOH solution. Drain a small amount of NaOH solution so it fills the buret tip and leaves the NaOH at the 0.00 mL level of the buret. WARNING: Sodium hydroxide solution is caustic. Avoid spilling it on your skin or clothing.

8.	You are now ready to perform the titration. This process is faster if one person operates the buret and another person operates the LabQuest.

- Start data collection.

- Before you have added any drops of NaOH solution, tap Keep and enter 0 as the buret volume in mL. Select OK to store the first data pair for this experiment.

- Add the next increment of NaOH titrant (enough to raise the pH about 0.15 units). When the pH stabilizes, tap Keep, enter the current buret reading (to the nearest 0.01 mL), and then select OK. You have now saved the second data pair for the experiment.

- Continue adding NaOH solution in increments that raise the pH by about 0.15 units and enter the buret reading after each increment. When a pH value of approximately 3.5 is reached, change to a one-drop increment. Enter a new buret reading after each increment. Note: It is important that all increment volumes in this part of the titration be equal; that is, one-drop increments.

- After a pH value of approximately 10 is reached, again add larger increments that raise the pH by about 0.15 pH units, and enter the buret level after each increment.

- Continue adding NaOH solution until the pH value remains constant.

9.	Stop data collection.

10.	Examine the data on the displayed graph of pH vs. volume to find the equivalence point—that is the largest increase in pH upon the addition of 1 drop of NaOH solution. Tap any data point. near the region of the graph with the largest increase in pH. Find the NaOH volume just before this jump. Record this value. Then record the NaOH volume after the drop producing the largest pH increase was added.

11.	Dispose of the beaker contents as directed by your instructor. Rinse the Go Wireless pH and return it to the pH storage solution.

METHOD 2:  Measuring Volume with a Drop Counter

1.	Obtain and wear goggles.

2.	Add 40 mL of distilled water to a 100 mL beaker. Use a pipet bulb (or pipet pump) to pipet 5.00 mL of the HCl solution into the 100 mL beaker with distilled water. DANGER: Handle the hydrochloric acid with care. It can cause painful burns if it comes in contact with the skin.

3.	Obtain approximately 40 mL of ~0.1 M NaOH solution in a 250 mL beaker. Record the precise NaOH concentration. WARNING: Sodium hydroxide solution is caustic. Avoid spilling it on your skin or clothing.

4.	Obtain the plastic 60 mL reagent reservoir. Close both valves by turning the handles to a horizontal position.

Rinse the reservoir with a few mL of the ~0.1 M NaOH solution. Use a utility clamp to attach the reagent reservoir to the ring stand. Add the remainder of the NaOH solution to the reagent reservoir.

Drain a small amount of NaOH solution into the 250 mL beaker so it fills the reservoir’s tip. To do this, turn both valve handles to the vertical position for a moment, then turn them both back to horizontal.

5.	Connect Go Wireless pH. Lower the Drop Counter onto a ring stand and connect it to 
DIG 1. Choose New from the File menu.

To connect Go Wireless pH:

- Press the power button on the Go Wireless Electrode Amplifier to turn it on. The LED on the sensor will flash red.

- Choose New from the File menu. On the Meter screen, choose Wireless Device Setup > Go Wireless… from the Sensors menu. Select your Go Wireless pH from the list of available sensors. When the sensor is paired with the software, the sensor LED will flash green.

6.	Calibrate the Drop Counter.

- Choose Calibrate ► Drop Counter from the Sensors menu:

- If you want to use the results from a previous calibration, tap Equation. Enter the values for Drops/mL. Select Apply, then OK. Proceed directly to Step 7.

- If you want to perform a new calibration, continue with this step.

- Select Calibrate Now.

- Place a 10 mL graduated cylinder directly below the slot on the Drop Counter, lining it up with the tip of the reagent reservoir.

- Open the bottom valve on the reagent reservoir (vertical). Keep the top valve closed (horizontal).

- Slowly open the top valve of the reagent reservoir so that drops are released at a slow rate (2–3 seconds per drop). You should see the drops being counted on the screen.

- When the volume of NaOH solution in the graduated cylinder is between 9 and 10 mL, close the bottom valve of the reagent reservoir.

- Enter the precise Volume of NaOH. Select Stop, and then select OK.

7.	Discard the NaOH solution in the graduated cylinder as indicated by your instructor and set the graduated cylinder aside.

8.	Assemble the apparatus.

- Set up the ring stand with stir plate or the Stir Station.

- Insert Go Wireless pH through the large hole in the Drop Counter.

- Attach the Microstirrer to the bottom of the pH Electrode, as shown in the small picture. Rotate the paddle wheel of the Microstirrer and make sure that it does not touch the bulb of the pH Electrode.

- Adjust the positions of the Drop Counter and reagent reservoir so they are both lined up to the center of the magnetic stirrer.

- Lift up Go Wireless pH, and slide the beaker containing the HCl solution onto the magnetic stirrer. Lower Go Wireless pH into the beaker.

- Adjust the position of the Drop Counter so that the Microstirrer on the electrode is just touching the bottom of the beaker.

- Adjust the reagent reservoir so its tip is just above the Drop Counter slot.

9.	Turn on the magnetic stirrer so that the Microstirrer is stirring at a fast rate.

10.	Start data collection. Fully open the bottom valve. When the first drop passes through the Drop Counter slot, check the graph to see that the first data pair was recorded. Make sure the drops are released at a slow rate (2–3 seconds per drop) for proper data collection.

11.	Observe the graph. Note when a large increase in pH takes place—the equivalence point of the reaction. Let the titration proceed for 3–4 milliliters beyond the equivalence point, and then stop data collection. Close the bottom valve of the reagent reservoir.

12.	Dispose of the beaker contents as directed by your instructor.

13.	Examine the data on the displayed graph of pH vs. volume to find the equivalence point. Move to the region of the graph with the largest increase in pH. Find the NaOH volume just before this jump. Record this value in the data table. Then record the NaOH volume after the drop producing the largest pH increase was added.

14.	If time permits, repeat the procedure.

alternate equivalence point method

An alternate way of determining the precise equivalence point of the titration is to take the first and second derivatives of the pH-volume data.

1.	Determine the peak value on the first derivative vs. volume plot.

- Tap the Table tab. Choose New Calculated Column from the Table menu.

- Enter d1 as the Calculated Column Name. Select the equation, 1st derivative (Y,X). Use Volume as the Column for X, and pH as the Column for Y. Select OK.

- On the displayed plot of d1 vs. volume, examine the graph to determine the volume at the peak value of the first derivative.

2.	Determine the zero value on the second derivative vs. volume plot.

- Tap the Table tab. Choose New Calculated Column from the Table menu.

- Enter d2 as the Calculated Column Name. Select the equation, 2nd derivative (Y,X). Use Volume as the Column for X, and pH as the Column for Y. Select OK.

- On the displayed plot of d2 vs. volume, examine the graph to determine the volume when the 2nd derivative equals approximately zero.

Processing the data

1.	Use your printed graph and data table to confirm the volume of NaOH titrant you recorded before and after the largest increase in pH values upon the addition of 1 drop of NaOH solution.

2.	Determine the volume of NaOH added at the equivalence point. To do this, add the two NaOH values determined above and divide by two.