## Slide 1
Wind Energy for Students
The Kidwind Project
www.kidwind.org
Copyright 2008
Notes: <number>

## Slide 2: Electricity!
How much would it cost to run this 100 Watt bulb for a full day (24 hrs)?
100 Watts x 24 hours = 2400 Watt Hours (2400 Watt Hours = 2.4 Kilowatt Hours)
2.4 kWh x $0.08/kWh = $0.19
What about this 25 Watt CFL light bulb, which produces the same amount of light?
25 Watts x 24 hours = 600 Watt Hours (600 Watt Hours = 0.6 Kilowatt Hours)
0.6 kWh x $0.08/kWh = $0.05
More efficient light bulbs are great, but what is the BEST way to conserve electricity and reduce our consumption of fossil fuels???
TURN IT OFF!!!
Be conscious of your energy choices!
Notes: <number>

## Slide 3: Where do we get our electricity?
Notes: <number>
<number>

## Slide 4: What is a Fossil Fuel???
Notes: <number>

## Slide 5: What is “Renewable Energy?”
Notes: <number>

## Slide 6: Types of Electricity Generating Windmills
Small (10 kW)
Homes
Farms
Remote Applications
(e.g. water pumping, telecom sites, icemaking)
Large (250 kW - 2+MW)
Central Station Wind Farms
Distributed Power
Intermediate
(10-250 kW)
Village Power
Hybrid Systems
Distributed Power
Notes: <number>

## Slide 7: Parts of a Wind Turbine
Notes: <number>

## Slide 8
Notes: <number>

## Slide 9: Wind Turbine Perspective
Nacelle
56 tons
Tower
3 sections
Workers
Blade
112’ long

## Slide 10
150 m2
250 m2
800 m2
1,800 m2
3,700 m2
1980
1985
1990
1995
2000
A= 12,000 m2
2005
How big will wind turbines be?
2010
Slide courtesy NREL
Notes: <number>

## Slide 11: Large Wind Turbines
450’ base to blade
Each blade 112’
Span greater than 747
163+ tons total
Foundation 20+ feet deep
Rated at 1.5 – 5 megawatt
Supply at least 350 homes
Notes: <number>

## Slide 12
Yawing – Facing the Wind
Active Yaw (all medium & large turbines produced today, & some small turbines from Europe)
  Anemometer on nacelle tells controller which way to point rotor into the wind
  Yaw drive turns gears to point rotor into wind
Passive Yaw (Most small turbines)
  Wind forces alone direct rotor
    Tail vanes
    Downwind turbines
Notes: <number>

## Slide 13
Notes: <number>
Note where wind energy projects are located….
CA, TX are the leaders…IA, MN and WA are the next batch….
Projects tend to be where the wind is located….not a whole lot in the SE

## Slide 14
Notes: <number>
Notice where the winds are the strongest….
MN, ND, SD called the Saudia Arabia of windpower…if we saturated these state with wind turbine we could generate at most of energy used in the US…Why have we not done this? Tranmission is one major problem need to match load with generation…how would we get all the power out of there?
Why don’t we put lots of wind farms in the rockies? Lots of wind but very hard to get at 60 meter long blade to the continental divide….logisitics of these large machines is very challenging!

## Slide 15: Why do windmills need to be high in the sky??
Notes: <number>
The higher we get the more faster and cleaner the wind are.
As you move closer to the earth the friction with the surface of the earth causes the wind to slow down and to become more turbulent…bad things if you want to generate energy from the wind. The nacelle of most commercial wind turbines is around 100 meters.

## Slide 16: Importance of Wind Speed
No other factor is more important to the amount of power available in the wind than the speed of the wind
Power is a cubic function of wind speed
  V X V X V
20% increase in wind speed means 73% more power
Doubling wind speed means 8 times more power
Notes: <number>

## Slide 17: Calculation of Wind Power
Power in the wind
  Effect of air density, 
  Effect of swept area, A
  Effect of wind speed, V
R
Swept Area: A = πR2 Area of the circle swept by the rotor (m2).
Power in the Wind = ½ρAV3
Notes: <number>
This is the equation for the power in the wind. (Don’t fear – there are only 2 equations in this presentation.) Each of the terms in this equation can tell us a lot about wind turbines and how they work. Lets look at wind speed (V), swept area (A), and density (Greek letter “rho,” ) one at a time.
First, let’s look at wind speed, V. Because V is cubed in the equation, a small increase in V makes for a increase in power. (illustrated on next slide)
(Click on the links at the bottom to get the values of both k and .)

## Slide 18: Carnage!
Notes: <number>

## Slide 19: Jobs in the Wind Industry
Notes: <number>

## Slide 20: Construction
Notes: <number>

## Slide 21: Operations/Maintenance
Notes: <number>

## Slide 22: Engineering/Design
Notes: <number>

## Slide 23: Public Relations/Organizing Support
Notes: <number>

## Slide 24: Environmental Impact Assessment
Notes: <number>

## Slide 25
Questions???
Notes: <number>