## Slide 1
Wind Turbine Blade Design
Joseph Rand
The Kidwind Project
joe@kidwind.org
877-917-0079
Notes: <number>

## Slide 2
Notes: <number>
A look inside. Blades are a very important component (duh!)
Things to note as compared to Small Wind Turbines
Blades can be actively pitched by hydraulics. Spin at 12-20 RPM --- much slower than a small wind turbine
Large driveshaft attached to a gearbox….must go from 12-20 RPM to 1600 RPM for the generator.
Generator creates electricity.
Small Wind Turbines use vanes (typcally) to track the wind…they uses and anemometer and hydraulics to move the turbine.
Highly computerized and automated….senses conditions and can turn itself off if there is a problem.
Often connected by computers to one location and run from there.

## Slide 3: Calculation of Wind Power
Power in the wind
  Effect of swept area, A
  Effect of wind speed, V
  Effect of air density, 
R
Swept Area: A = πR2 Area of the circle swept by the rotor (m2).
Power in the Wind = ½ρAV3
Notes: <number>
This is the equation for the power in the wind. (Don’t fear – there are only 2 equations in this presentation.) Each of the terms in this equation can tell us a lot about wind turbines and how they work. Lets look at wind speed (V), swept area (A), and density (Greek letter “rho,” ) one at a time.
First, let’s look at wind speed, V. Because V is cubed in the equation, a small increase in V makes for a increase in power. (illustrated on next slide)
(Click on the links at the bottom to get the values of both k and .)

## Slide 4: Many Different Rotors…
KidWind Project | www.kidwind.org
Notes: Various rotor configurations… all used to convert wind into usable energy.
Why do the rotors differ so greatly? Why have we come to use the typical 3-blade rotor in nearly all industrial wind turbines today?
<number>

## Slide 5: Number of Blades – One
Rotor must move more rapidly to capture same amount of wind
  Gearbox ratio reduced
  Added weight of counterbalance negates some benefits of lighter design
  Higher speed means more noise, visual, and wildlife impacts
Blades easier to install because entire rotor can be assembled on ground
Captures 10% less energy than two blade design
Ultimately provide no cost savings
Notes: <number>

## Slide 6: Number of Blades - Two
Advantages & disadvantages similar to one blade
Need teetering hub and or shock absorbers because of gyroscopic imbalances
Capture 5% less energy than three blade designs
Notes: <number>

## Slide 7: Number of Blades - Three
Balance of gyroscopic forces
Slower rotation
  increases gearbox & transmission costs
  More aesthetic, less noise, fewer bird strikes
Notes: <number>

## Slide 8: Blade Composition Wood
Wood
  Strong, light weight, cheap, abundant, flexible
  Popular on do-it yourself turbines
Solid plank
Laminates
Veneers
Composites
Notes: <number>

## Slide 9: Blade Composition Metal
Steel
  Heavy & expensive
Aluminum
  Lighter-weight and easy to work with
  Expensive
  Subject to metal fatigue
Notes: <number>

## Slide 10: Blade Construction Fiberglass
Lightweight, strong, inexpensive, good fatigue characteristics
Variety of manufacturing processes
  Cloth over frame
  Pultrusion
  Filament winding to produce spars
Most modern large turbines use fiberglass
Notes: <number>

## Slide 11
KidWind Project | www.kidwind.org
Notes: <number>

## Slide 12
KidWind Project | www.kidwind.org
Notes: These “scimitar” shaped blades are designed to be efficient while also reducing NOISE coming off the blades.
Since this is a downwind rotor there are more variables to consider… downwind turbines can be noisier and experience turbulent wind going around the tower.
<number>

## Slide 13: Lift & Drag Forces
The Lift Force is perpendicular to the direction of motion. We want to make this force BIG.
The Drag Force is parallel to the direction of motion. We want to make this force small.
α = low
α = medium
<10 degrees
α = High
Stall!!
Notes: <number>

## Slide 14
Airfoil Shape
Just like the wings of an airplane, wind turbine blades use the airfoil shape to create lift and maximize efficiency.
The Bernoulli Effect
Notes: <number>

## Slide 15: Lift/Drag Forces Experienced by Turbine Blades
KidWind Project | www.kidwind.org
Notes: These vectors represent the forces experienced by an airfoil wind turbine blade as it rotates.
Notice that the “apparent wind” is a combination of the “real wind” and the “head wind”
Well designed blades should minimize the drag force.
<number>

## Slide 16: Twist & Taper
Speed through the air of a point on the blade changes with distance from hub
Therefore, tip speed ratio varies as well
To optimize angle of attack all along blade, it must twist from root to tip
Fast
Faster
Fastest
Notes: <number>

## Slide 17: Tip-Speed Ratio
Tip-speed ratio is the ratio of the speed of the rotating blade tip to the speed of the free stream wind.
There is an optimum angle of attack which creates the highest lift to drag ratio.
Because angle of attack is dependant on wind speed, there is an optimum tip-speed ratio
ΩR
V
TSR =
Where,
Ω = rotational speed in radians /sec
R = Rotor Radius
V = Wind “Free Stream” Velocity
ΩR
R

## Slide 18
Performance Over Range of Tip Speed Ratios
Power Coefficient Varies with Tip Speed Ratio
Characterized by Cp vs Tip Speed Ratio Curve
Notes: <number>

## Slide 19: Betz Limit
All wind power cannot be captured by rotor or air would be completely still behind rotor and not allow more wind to pass through.
Theoretical limit of rotor efficiency is 59%
Most modern wind turbines are in the 35 – 45% range
Notes: <number>

## Slide 20: Rotor Solidity
Solidity is the ratio of total rotor planform area to total swept area
Low solidity (0.10) = high speed, low torque
High solidity (>0.80) = low speed, high torque
A
R
a
Solidity = 3a/A
Notes: <number>

## Slide 21
KidWind Project | www.kidwind.org
Pitch Control Mechanisms
Notes: <number>

## Slide 22: Some Wacky Ideas…
Notes: <number>

## Slide 23: Manufacturing Blades
The blade mold (left) is lined with layers of fiberglass, then injected with epoxy resin. To enhance stiffness, a layer of wood is placed between the fiberglass layers. The two molds are joined and adhered together using a special liquid epoxy, which evenly joins the two sides of the blade.
Finally, the whole mold is baked like a cake! 8 hours at 70 degrees C.
Notes: <number>

## Slide 24: Manufacturing Blades
Before delivery, samples of the rotor blades have to go through a variety of static and dynamic tests. First, they are subjected to 1.3 times the maximum operating load. To simulate 20 years of material fatigue, the blades are then mounted on special test beds and made to vibrate around two million times, before the endurance of the material is again tested with a final static test.
The blades are painted white, then shipped to wind farms all over the world.
Notes: <number>

## Slide 25: Advanced Classroom Blades
Cardboard Tube for twisted blades
Airfoil Blades
Notes: <number>

## Slide 26: Wind Turbine Blade Challenge
Students perform experiments and design different wind turbine blades
Use simple wind turbine models
Test one variable while holding others constant
Record performance with a multimeter or other load device
Goals: Produce the most voltage, pump the most water, lift the most weight
  Minimize Drag
  Maximize LIFT
  Harness the POWER of the wind!
Notes: <number>

## Slide 27: Questions?
Joe Rand
KidWind Project
joe@kidwind.org
Notes: <number>