## Slide 1
WIND TURBINE TECHNOLOGY
SMALL AND LARGE
KidWind Project
www.kidwind.org

## Slide 5: Calculation of Wind Power
Power in the wind
  Effect of swept area, A
  Effect of wind speed, V
  Effect of air density, 
R
Swept Area: A = πR2 Area of the circle swept by the rotor (m2).
Power in the Wind = ½ρAV3
Notes: This is the equation for the power in the wind. (Don’t fear – there are only 2 equations in this presentation.) Each of the terms in this equation can tell us a lot about wind turbines and how they work. Lets look at wind speed (V), swept area (A), and density (Greek letter “rho,” ) one at a time.
First, let’s look at wind speed, V. Because V is cubed in the equation, a small increase in V makes for a increase in power. (illustrated on next slide)
(Click on the links at the bottom to get the values of both k and .)

## Slide 7: Types of Wind Turbines
Vertical Axis
Horizontal Axis
Notes: Turbines can be categorized in two overarching classes based on the orientation of the rotor. The rotor can spin on a vertical axis or a horizontal axis.
Vertical Axis Wind Turbines (aka VAWTs)
Horizontal Axis Wind Turbines (aka HAWTs)

## Slide 8: Vertical Axis Wind Turbines (VAWTs)
Make up a (very) small percentage of installed wind turbines
Often marketed for “urban,” “turbulent,” “low-wind,” or even “rooftop” applications
No certified VAWTs
Overall poor performance and reliability
Overall not successful in the market (though very few small wind turbines are!)

## Slide 9: SMALL WIND

## Slide 10
Small wind:
Wind turbines with a capacity rating of less than or equal to 100 kW. Turbines in this category range in size from smaller than 1 kW for off-grid applications to 100-kW turbines that can provide village power.

## Slide 11: Modern Small Wind Turbines: High Tech, High Reliability, Low Maintenance
Technically advanced
Only ~3 Moving Parts
Low maintenance requirements
Over 69,000 small wind turbines across U.S.
American companies are the market and technology leaders
Notes: When teachers build their Basic PVC Turbines they are more like a small wind turbine, simple direct drive systems.
Emphasize high RPM…these things spin fast 300-600 RPM.
Many of these are sent to villages offshore as they can provide power for an entire village…here in the US is hard to justify the cost for one household. $$ on small wind turbines 10K-100K

## Slide 12: Off-Grid vs. Grid-Tied

## Slide 13: Good, bad, ugly…?
Notes: For more info www.bergey.com, www.windenergy.com

## Slide 14: Small Wind Certification Council

## Slide 15: Over-Speed Protection During High Winds
Upward Furling: The rotor tilts back during high winds
Side Furling: The rotor turns up and to one side

## Slide 16: Small Wind Towers

## Slide 17: More tower, more power!

## Slide 18: Maintenance …not for the faint of heart

## Slide 19: Wind Turbine Siting

## Slide 21: UTILITY SCALE WIND TURBINES

## Slide 22: Evolution of U.S. Utility-Scale Wind

## Slide 23: Modern Large Wind Turbines
Rated Power: 1 – 5 Megawatts (MW)
Wind Speeds: 3 – 25 m/s
  Rated Power at 11-12 m/s
Steel tubular tower
Installed in plants/farms of 100-200 MW

## Slide 25: How much energy?
Capacity Factor:
Quantity of electricity a generator actually produces relative to the maximum it could produce at continuous full power operation during the same period.
Typical large wind turbine capacity factor: 30-40%
  2 MW wind turbine may generate about 7,000,000 kWh per year
    (2,000 kW * 24 hours/day
    * 365 days/year * 0.4 CF)

## Slide 26: Installed Cost of Wind Energy

## Slide 28
Blade Pitch Controller
Low Speed Shaft
Gearbox
High Speed Shaft
Generator
Yaw Controller
Notes: Power coming off a utility turbine is synced to the grid.
Blade pitch controller can make minor adjustments to change torque, rpm and protect the turbine in high winds.
Typical gear ratio may be 80:1 or 100:1
Generators typically use induction – or electromagnets – rather than permanent magnets.
High speed shaft may spin the generator at 1600+ rpm.

## Slide 29: Active Blade Pitching

## Slide 30: Geared vs. Direct Drive

## Slide 31: OFFSHORE WIND

## Slide 35: Power Curve & Annual Energy Output

## Slide 36: Betz Limit
All wind power cannot be captured by rotor or air would be completely still behind rotor and not allow more wind to pass through.
Theoretical limit of rotor efficiency is 59%
Most modern wind turbines are in the 35 – 45% range

## Slide 37: Wind Turbine Blade Design
Fast
Faster
Fastest

## Slide 38: Lift/Drag Forces Experienced by Turbine Blades
Notes: These vectors represent the forces experienced by an airfoil wind turbine blade as it rotates.
Notice that the “apparent wind” is a combination of the “real wind” and the “head wind”
Well designed blades should minimize the drag force.

## Slide 39: Rotor Solidity
Solidity is the ratio of total rotor planform area to total swept area
Low solidity (0.10) = high RPM, low torque
High solidity (>0.80) = low RPM, high torque
A
R
a
Solidity = 3a/A

## Slide 40
KidWind Project
www.kidwind.org